## Slide 1: CSE 331: Microprocessor Interfacing and Embedded Systems
Lecture 4: Bitwise Operation Instructions

## Slide 2: Overview
Logic Instructions
Shifts and Rotates
ARM Arithmetic Datapath

## Slide 3: Logical Operators
Basic logical operators:
  AND: outputs 1 only if both inputs are 1
  OR: outputs 1 if at least one input is 1
  XOR: outputs 1 if exactly one input is 1
In general, can define them to accept >2 inputs, but in the case of ARM assembly, both of these accept exactly 2 inputs and produce 1 output
  Again, rigid syntax, simpler hardware

## Slide 4: Logical Operators
Truth Table: standard table listing all possible combinations of inputs and resultant output for each
Truth Table for AND, OR and XOR, BIC (Bit Clear)
A B A AND B
A OR B
A XOR B A BIC B
0 0
0 1
1 0
1 1
0
1
1
1
0
0
0
1
0
1
1
0
0
0
1
0

## Slide 5: Uses for Logical Operators
Note that ANDing a bit with 0 produces a 0 at the
output while ANDing a bit with 1 produces the original bit.
This can be used to create a mask.
  Example:
1011 0110 1010 0100 0011
0000 0000 0000 0000 0000
1101 1001 1010
1111 1111 1111
1101 1001 1010
The result of ANDing these:
0000 0000 0000 0000 0000
mask:
mask last 12 bits

## Slide 6: Uses for Logical Operators
Similarly, note that ORing a bit with 1
produces a 1 at the output while ORing a bit with 0 produces the original bit.
This can be used to force certain bits of a string to 1s.
  For example, 0x12345678 OR 0x0000FFFF results in 0x1234FFFF (e.g. the high-order 16 bits are untouched, while the low-order 16 bits are forced to 1s).

## Slide 7: Uses for Logical Operators
Additionally, note that XORing a bit with 1 produces flips the bit (0 -> 1, 1 -> 0) at the output while XORing a bit with 0 produces
the original bit.
It tells whether two bits are unequal.
It is an optional bit-flipper (the deciding input chooses whether to invert the data input).

## Slide 8: Uses for Logical Operators
Finally, note that BICing a bit with 1 resets
the bit (sets to 0) at the output while BICing a bit with 0 produces the original bit.
This can be used to force certain bits of a string to 0s.
  For example, 0x12345678 BIC 0x0000FFFF results in 0x12340000 (e.g. the high-order 16 bits are untouched, while the low-order 16 bits are forced to 0s).

## Slide 9: Bitwise Logic Instruction Syntax
Syntax of Instructions:
1 2, 3, 4
where:
  instruction by name
  operand getting result (“destination”)
  1st operand for operation (“source1”)
  2nd operand for operation (“source2”)
Syntax is rigid (for the most part):
1 operator, 3 operands
Why? Keep Hardware simple via regularity

## Slide 10: Bitwise Logic Operations
Bitwise AND in Assembly
  Example: AND r0,r1,r2 (in ARM) Equivalent to: a = b & c (in C)
where ARM registers r0,r1,r2 are associated with C variables a, b, c
Bitwise OR in Assembly
Example: ORR | r3, | r4, | r5 (in ARM)
Equivalent to: d = | e ¦ | f (in | C)
where ARM registers r3,r4,r5 are associated with C variables d, e, f

## Slide 11: Bitwise Logic Operations
Bitwise XOR in Assembly
  Example: EOR r0,r1,r2 (in ARM) Equivalent to: a = b ^ c (in C)
where ARM registers r0,r1,r2 are associated with C variables a, b, c
Bitwise Clear in Assembly
Example: BIC | r3, | r4, | r5 (in ARM)
Equivalent to: d = | e & | (!f) | (in C)
where ARM registers r3,r4,r5 are associated with C variables d, e, f

## Slide 12: Assignment Instructions
Assignment in Assembly
Example: | MOV | r0,r1 | (in ARM)
Equivalent to: | a = | b | (in C)
where ARM registers r0 are associated with C variables a
Example: | MOV | r0,#10 | (in ARM)
Equivalent to: a = | 10 |  | (in C)

## Slide 13: Assignment Instructions
MVN – Move Negative – moves one complement of the operand into the register.
Assignment in Assembly
Example:
Equivalent to:
MVN r0,#0 a = -1
(in ARM)
(in C)
where ARM registers r0 are associated with C variables a
Since ~0x00000000 == 0xFFFFFFFF

## Slide 14: Shifts and Rotates
LSL – logical shift left by n bits – multiplication by 2n
LSR–logical shift right by n bits–unsigned division by 2n
ASR – arithmetic shift right by n bits – signed division by 2n
ROR – rotate right by n bits – 32 bit rotate
 |  |  | … |  |  | 
0
C
 |  |  | … |  |  | 
0
C
 |  |  | … |  |  | 
C
…

## Slide 15: Shifts and Rotates
MOV | r4, | r6, | LSL | #4 | ; | r4 | = | r6 | << | 4
MOV | r4, | r6, | LSR | #8 | ; | r4 | = | r6 | << | 8
Shifting in Assembly
Examples:
Rotating in Assembly
Examples:
MOV r4, r6, ROR #12
; r4 = r6 rotated right 12 bits
; r4 = r6 rotated left by 20 bits (32 -12)
Therefore no need for rotate left.

## Slide 16: Variable Shifts and Rotates
Also possible to shift by the value of a register
Examples:
MOV r4, r6, LSL r3
; r4 = r6 << value specified in r3 MOV r4, r6, LSR #8 ; r4 = r6 >> 8

## Slide 17: Constant Multiplication
Constant multiplication is often faster using shifts and additions
MUL r0, r2, #8 ; r0 = r2 * 8
Is the same as:
MOV r0, r2, LSL #3 ; r0 = r2 * 8
Constant division
Vs. | MOV | r1, | r3, | ASR | #7 | ; | r1 | = | r3/128
 | MOV | r1, | r3, | LSR | #7 | ; | r1 | = | r3/128
The first treats the registers like signed values (shifts in MSB). Thelatter treats data like unsigned values (shifts in 0). int vs unsigned int >>

## Slide 18: Constant Multiplication
Constant multiplication with subtractions
MUL r0, r2, #7 ; r0 = r2 * 7
Is the same as:
RSB r0, r2, r2, LSL #3 ; r0 = r2 * 7
; r0 = -r2 + 8*r2 = 7*r2 RSB r0, r1, r2 is the same as
SUB r0, r2, r1 ; r0 = r2 – r1
Multiply by 35:
ADD r9,r8,r8,LSL #2; r9=r8*5
RSB r10,r9,r9,LSL #3 ; r10=r9*7

## Slide 19: Conclusion
Instructions so far:
  Previously:
ADD, SUB, RSB MUL, MULA, [U|S]MULL, [U|S]MLAL
  New instructions:
AND, | ORR, | EOR, | BIC
MOV, | MVN |  | 
LSL, | LSR, | ASR, | ROR
Shifting can only be done on the second source operand
Constant multiplications possible using shifts and addition/subtractions