## Slide 1: CSE 331: Microprocessor Interfacing and Embedded Systems
Lecture 6: Procedures

## Slide 2: C functions
main() {
int ... | a,b,c; | compiler/programmer keep track of?
c = | sum(a,b);/* | a,b,c:r0,r1,r2*/
... } |  | 
/* really dumb sum function */ int sum(int x, int y) {
return x+y;
}
What information must
What instructions can accomplish this?

## Slide 3: Function Call Bookkeeping
Registers play a major role in keeping track of information for function calls
Register conventions:
Return address | lr | 
Arguments | r0, | r1, | r2, | r3
Return value | r0, | r1, | r2, | r3
Local variables | r4, | r5, | … , | r12
The stack is also used; more later

## Slide 4: Register Usage
r4
r5
r6
r7
r8
r9/sb
r10/sl
r11
r12
r13/sp
r14/lr
r15/pc
r0
r1
r2
r3
Register variables Must be preserved
Arguments into function Result(s) from function otherwise corruptible (Additional parameters
passed on stack)
Scratch register (corruptible)
Stack Pointer Link Register Program Counter
The compiler has a set of rules known as a Procedure Call Standard that determine how to pass parameters to a function (see AAPCS)
CPSR flags may be corrupted by function call. Assembler code which links with compiled code must follow the AAPCS at external interfaces
The AAPCS is part of the new ABI for the ARM Architecture
Register
Stack base
Stack limit if software stack checking selected
SP should always be 8-byte (2 word) aligned
R14 can be used as a temporary once value stacked

## Slide 5: Instruction Support for Functions
... sum(a,b);... /* a,b:$r3,$r4 */
C }
int sum(int x, int y) {return x+y; }
}
ARM
Address
1000
1004
1008
1012
1016
In ARM, all instructions are stored in memory just like data. So here we show the addresses of where the programs are stored.

## Slide 6: Instruction Support for Functions
... sum(a,b);... /* a,b:r4,r5 */
}
int sum(int x, int y) { return x+y;
}
address 1000 MOV
1004 MOV
1008 MOV
1012 B
1016 ...
r0,r4 r1,r5 lr,1016
sum
; x = a
; y = b
; lr = 1016
; branch to sum
2000 sum: ADD r0,r0,r1
2004 BX lr // MOV pc,lr i.e., return
C
A R M

## Slide 7: Instruction Support for Functions
2000 sum: ADD r0,r0,r1
2004 BX lr ; new instruction
... sum(a,b);... /* a,b:$s0,$s1 */
}
C int sum(int x, int y) { return x+y;
}
A R M
Question: Why use BX here? Why not simply use B?
Answer: sum might be called by many functions, so we can’t return to a fixed place. The calling proc to sum must be able to say“return here”somehow.

## Slide 8: Instruction Support for Functions
Single instruction to jump and save return address: jump and link (BL)
Before:
1008 | MOV lr, | 1016 ; lr=1016 | 
1012 | B sum | ; goto sum | 
After: 1008 | BL sum | # lr=1012, goto | sum
Why have a BL? Make the common case fast: function calls are very common. Also, you don’t have to know where the code is loaded into
memory with BL.

## Slide 9: Instruction Support for Functions
Syntax for BL (branch and link) is same as for B (branc):
BL label
BL functionality:
  Step 1 (link): Save address of next instruction into lr (Why next instruction? Why not current one?)
  Step 2 (branch): Branch to the given label

## Slide 10: Instruction Support for Functions
Syntax for BX (branch and exchange):
BX register
Instead of providing a label to jump to, the BX instruction provides a register which contains an address to jump to
Only useful if we know exact address to jump
Very useful for function calls:
  BL stores return address in register (lr)
  BX lr jumps back to that address

## Slide 11: Nested Procedures
int sumSquare(int x, int y) { return mult(x,x)+ y;
}
Something called sumSquare, now
sumSquare is calling mult.
So there’s a value in lr that sumSquare wants to jump back to, but this will be overwritten by the call to mult.
Need to save sumSquare return address before call to mult.

## Slide 12: Nested Procedures
In general, may need to save some other info in addition to lr.
When a C program is run, there are 3 important memory areas allocated:
  Static: Variables declared once per program, cease to exist only after execution completes. E.g., C globals
  Heap: Variables declared dynamically
  Stack: Space to be used by procedure during execution; this is where we can save register values

## Slide 13: C Memory Allocation
0
Code
Static
Heap
Explicitly created space, e.g., malloc(); C pointers
Variables declared once per program
Program
Address ∞
sp stack pointer
Stack
Space for saved procedure information

## Slide 14: Using the Stack
So we have a register sp which always points to the last used space in the stack.
To use stack, we decrement this pointer by the amount of space we need and then fill it with info.
So, how do we compile this?
int sumSquare(int x, int y) { return mult(x,x)+ y;
}

## Slide 15: Using the Stack
Hand-compile
sumSquare:
; restore stack
ADD sp,sp,#8
BX lr
mult: mul r0,r0,r0
BX lr
int sumSquare(int x, int y) { return mult(x,x)+ y; }
“push”
ADD | sp,sp,#-8 | ; | space | on | stack
 | STR lr,[sp,#4] | ; | save | ret | addr
STR | r1, [sp] | ; | save | y | 
BL | mult |  | ; | call | mult
LDR | r1, | [sp] ; | restore y |  | 
ADD r0,r0,r1 LDR lr, | ; mult()+y [sp, #4] | ; | get | ret | addr
“pop”
; return original location
; mult x,x

## Slide 16: Steps for Making a Procedure Call
Save necessary values onto stack (e.g. lr, r1)
Assign argument(s), if any
BL call
Restore values from stack
BX lr

## Slide 17: Rules for Procedures
Called with a BL instruction, returns with a
BX lr (or MOV pc, lr)
Accepts up to 4 arguments in r0, r1, r2 and r3
Return value is always in r0 (and if necessary in r1, r2, r3)
Must follow register conventions (even in functions that only you will call)! So what are they?

## Slide 18: ARM Registers
Register | Synonym | Role in Procedure Call Standard
r0-r1 | a1-a2 | Argument/Result/Scratch Register
r2-r3 | a3-a4 | Argument/Scratch Register
r4-r8 | v1-v5 | Variable Register
r9 | v6/sb/tr | Platform Register/Thread Register/Stack Base
r10-r11 | v7-v8 | Variable Register
r12 | ip | Intra-Procedure Call Scratch Register
r13 | sp | Stack Pointer
r14 | lr | Link Register
r15 | pc | Program Counter

## Slide 19: Register Conventions
CalleR: the calling function
CalleE: the function being called
When callee returns from executing, the caller needs to know which registers may have changed and which are guaranteed to be unchanged.
Register Conventions: A set of generally accepted rules as to which registers will be unchanged after a procedure call (BL) and which may be changed.

## Slide 20: Saved Register Conventions
r4-r11 (v1-v8): Restore if you change. Very important. If the callee changes these in any way, it must restore the original values before returning.
sp: Restore if you change. The stack pointer must point to the same place before and after the BL call, or else the caller won’t’be able to restore values from the stack.

## Slide 21: Volatile Register Conventions
lr: Can Change. The BX call itself will change this register. Caller needs to save on stack if nested call.
r0-r3 (a1-a4): Can change. These are
volatile argument registers. Caller needs to
save if they’ll need them after the call. E.g., r0 will change if there is a return value
r12 (ip) may be used by a linker as a scratch
register between a routine and any subroutine
it calls. It can also be used within a routine to
hold intermediate values between subroutine calls.

## Slide 22: Register Conventions
What do these conventions mean?
  If function R calls function E, then function R must save any temporary registers that it may be using onto the stack before making a BL call.
  Function E must save any saved registers it intends to use before garbling up their values
  Remember: Caller/callee need to save only volatile/saved registers they are using, not all registers.

## Slide 23: Basic Structure of a Function
;save lr
...
Prologue
entry_label:
ADD sp,sp, -framesize
STR lr, [sp, #framesize-4] save other regs if need be
;restore lr
LDR lr, [$sp, framesize-4] ADD sp,sp, #framesize
BX lr
Epilogue
restore other regs if need be
Body (call other functions…)
ra
memory

## Slide 24: Example
main() {
int i,j,k,m; /* i-m:v1-v4 */
...
i | = | mult(j,k); | ... | 
m | = | mult(i,i); | ... | }
int mult (int mcand, int mlier){ int product;
product = 0;
while (mlier > 0) { product += mcand; mlier -= 1; }
return product;}

## Slide 25: Example
start:
MOV | a1,v2 | ; | arg1 | = | j
MOV | a2,v3 | ; | arg2 | = | k
; call mult
; i = mult()
BL mult MOV v1,a1
...
MOV a1,v1 MOV a2,v1
BL mult MOV v4,a1
...
done
; arg1 = i
; arg2 = i
; call mult
; m = mult()
main() {int i,j,k,m; /* i-m:v1-v4 */
i = mult(j,k); ...
m = mult(i,i); ... }

## Slide 26: Example
Notes:
  main function ends with done, not BX lr, so there’s no need to save lr onto stack
  All variables used in main function are saved registers, so there’s no need to save these onto stack

## Slide 27: Example
int mult (int mcand, int mlier){ int product = 0;
while (mlier > 0) { product += mcand; mlier -= 1; }
return product;}
mult: MOV a3,#0; prod=0
Loop: | CMP BLE | a2, Fin | #0 | ; ; | mlier == if mlier | 0? <= | 0 | goto | Fin
ADD | a3,a3,a1 | ; | product += | mcand
ADD | a2,a2,#-1 | ; | mlier -= 1 | 
B Loop ; goto Loop
Fin: MOV a1,a3 ; setup return value BX lr ; return

## Slide 28: Example
Notes:
  No BL calls are made from mult and we don’t use any saved registers, so we don’t need to save anything onto stack
  Temp registers are used for intermediate calculations (could have used saved registers, but would have to save the caller’s on the stack.)
  a2 is modified directly (instead of copying into a temp register) since we are free to change it
  Result is put into a1 (r0) before returning

## Slide 29: Conclusion
Functions are called with BL, and return with
BX lr.
The stack is your friend: Use it to save anything you need. Just be sure to leave it the way you found it.
Register Conventions: Each register has a purpose and limits to its usage. Learn these and follow them, even if you’re writing all the code yourself.

## Slide 30: Conclusion
Instructions so far:
  Previously:
ADD,SUB,MUL,MULA, [U|S]MULL, [U|S]MLAL, RSB
AND, ORR, EOR, BIC
MOV, MVN
LSL, LSR, ASR, ROR
CMP, B{EQ,NE,LT,LE,GT,GE}
LDR, LDR, STR, LDRB, STRB, LDRH, STRH
New:
BL, BX
Registers we know so far
  All of them!