## Slide 1: Lecture#7: Stack & Recursion (Chapter#8) Summer, 2025
Credit: Dr. Mohammad A. Qayum
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
CSE331: Microprocessor Interfacing and Embedded Systems

## Slide 2: Stack
A Last-In-First-Out data structure
Only allow to access the most recently added item
  Also called the top of the stack
Key operations:
  push (add item to stack)
  pop (remove top item from stack)

## Slide 3: Stack Growth Convention: Ascending vs Descending
  Descending stack: Stack grows towards low memory address
  Ascending stack: Stack grows towards high memory address

## Slide 4: Cortex-M Stack
stack pointer (SP) = R13
Cortex-M uses full descending stack
stack pointer
  decremented on PUSH
  incremented on POP
  SP starts at 0x20000200 for STM32-Discovery

## Slide 5: Stack
PUSH {Rd}
  SP = SP-4 ⟶ descending stack
  (*SP) = Rd ⟶ full stack (r8, r7, r6)
Push multiple registers
PUSH {r6, r7, r8}
They are equivalent.
PUSH {r8}
PUSH {r7}
PUSH {r6}
The order in which registers listed in the register list does not matter.
When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. is stored last.
PUSH {r7, r6, r8}

## Slide 6: Stack
POP {Rd}
  Rd = (*SP) ⟶ full stack
  SP = SP + 4 ⟶ Stack shrinks
Pop multiple registers
They are equivalent.
POP {r6}
POP {r7}
POP {r8}
POP {r6, r7, r8}
The order in which registers listed in the register list does not matter.
When popping multiple registers, these registers are automatically loaded by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.
POP {r8, r6, r7}

## Slide 7: Full Descending Stack
PUSH {r1, r3, r2, r7}
POP {r3, r1, r7, r2}

## Slide 8: Stack
PUSH {r3, r1, r7, r2}
POP {r3, r1, r7, r2}

## Slide 9: Stack
PUSH {r1, r2, r3, r7}
POP {r3, r1, r7, r2}

## Slide 10: Recursive Procedure Example
C code:
int fact (int n)
{
if (n <
1)
return 1;
else return n * fact(n - 1);
}

## Slide 11: Recursive Functions
push LR (& working registers) onto stack before nested call
pop LR (& working registers) off stack after nested return

## Slide 12: Recursive Factorial in Assembly
.global main
main:
MOV r0, #0x03
BL factorial
B stop
factorial: PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BGE NZ
MOVS r0, #0x01
loop: POP {r4, pc}
NZ: SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
3 * factorial(2)
2 * factorial(1)
1
return 2
return 6
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 13: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000130
0xFFFFFFFF
0x20000600
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x20000600
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
3
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 14: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial: PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BGE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000136
0x08000134
0x20000600
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x20000600
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
3
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 15: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BGE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000138
0x08000134
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
3
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Order in which registers are specified is not important: the lowest register is always stored at the lowest address

## Slide 16: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BGE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x0800013A
0x08000134
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
3
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 17: Recursive Factorial in Assembly
.global __main
__main:
MOV r0, #0x04
BL factorial
B stop
factorial: PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BGE NZ
MOVS r0, #0x01
loop: POP {r4, pc}
NZ: SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000144
0x08000134
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 18: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000136
0x08000148
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 19: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000138
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 20: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x0800013A
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 21: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BGE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000144
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 22: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000136
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 23: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000138
0x08000148
0x200005E8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x08000148
2
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 24: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x0800013A
0x08000148
0x200005E8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x08000148
2
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
1
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 25: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x0800013E
0x08000148
0x200005E8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x08000148
2
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
1
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 26: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000140
0x08000148
0x200005E8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x08000148
2
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
1
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 27: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000148
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
1
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 28: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x0800014C
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 29: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
stop B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000140
0x08000148
0x200005F0
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x08000148
3
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
2
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Order in which registers are specified is not important.

## Slide 30: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
stop B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000148
0x08000148
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
2
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 31: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
stop B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x0800014C
0x08000148
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
6
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 32: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
stop B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000140
0x08000148
0x200005F8
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x08000134
0x20000600
0
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
3
6
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 33: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop:
MOV r7, #1
SWI 0
0x08000130
0x08000134
0x08000134
0x08000148
0x20000600
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x20000600
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
6
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 34: Recursive Factorial in Assembly
.global __main
__main
MOV r0, #0x03
BL factorial
B stop
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
stop: MOV r7, #1
SWI 0
0x08000130
0x08000134
0x0800014E
0x08000148
0x20000600
pc
lr
sp
0x00000000
0xFFFFFFFF
Memory
Address
Data
0x20000600
0x12345678
…
…
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
6
r4
r0
…
…
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
0x0800014E

## Slide 35: Conclusion
Instructions so far:
  Previously:
ADD,SUB,MUL,MULA, [U|S]MULL, [U|S]MLAL, RSB
AND, ORR, EOR, BIC
MOV, MVN
LSL, LSR, ASR, ROR
CMP, B{EQ,NE,LT,LE,GT,GE}
LDR, STR, LDRB, STRB, LDRH, STRH
BL, BX
New:
PUSH, POP
Registers we know so far
  All of them!
Addressing mode so far
  Most of them!